## Solaris Hardware
Scan for new devices	devfsadm
List all HW	cfgadm -val
List all disks	iostat -En
Total physical memory	prtconf grep Memory
Openboot version	prtconf -V
Processor info	psrinfo -v
Dump device	dumpadm
Swap devices	swap -l
Swap usage	swap -s

Add hardware
- touch /reconfigure
- reboot
### Howto: Find Faulty Hardware
- From the service processor
  - As admin:
sc> showfaults -v
As root:
-> show faulty
- From console/ssh
  - View all faulty components:
# fmadm faulty
View detail, take UUID from above command:
# fmadm faulty -v -u {UUID}
### Howto: Find/Recover Bad Sectors
Unmount the disk (if it is the root disk boot into single-user or off a CD)
# format {Select the disk}
format> analyze
analyze> read
Once complete use the blocks identified above (does not work on all controllers or disks)
format> repair
Enter absolute block number of defect: 100
Ready to repair defect, continue? y
Repairing block 100 ...ok.
format> q
### Howto: fix prtdiag hangs
# svcadm -v disable svc:/system/picl:default
Wait for about a minute …
# svcadm -v enable svc:/system/picl:default
### Howto: Scrub disks for decommission
Determine how many disks are connected to the system using the format command. It is not necessary to scrub the SAN drives, only the local drives. So from the the format command output make note of the local disk with the highest number.
Use the highest local disk number above as the DISK parameter N in the script below. Create and run the following script to scrub the local disks.
DISKS=N
while [ $DISKS -ge 0
do
  echo disk>>/tmp/scrub
  echo $DISKS>>/tmp/scrub
  echo defect>>/tmp/scrub
  echo primary>>/tmp/scrub
  echo quit>>/tmp/scrub
  echo analyze>>/tmp/scrub
  echo purge>>/tmp/scrub
  echo quit>>/tmp/scrub
  echo defect>>/tmp/scrub
  echo both>>/tmp/scrub
  echo quit>>/tmp/scrub
  echo analyze>>/tmp/scrub
  echo purge>>/tmp/scrub
  echo quit>>/tmp/scrub
  (( DISKS -+ 1 ))
done
format -f /tmp/scrub
### ILOM/ALOM
Backup config Login to ILOM CLI as root user
-> cd /SP/config
-> set passphrase={passphrase}
-> set dump_uri=scp://user:passwd@ipaddr/path_to/save_file
Restore config Login to ILOM CLI as root user
-> cd /SP/config
-> set passphrase={passphrase}
-> set load_uri=scp://user:passwd@ipaddr/path_to/save_file
Setting IP address for first time Connect via serial connection, login as root user
-> cd /SP/network
-> set pendingipdiscovery=static
-> set pendingipaddress=ip_address
-> set pendingipnetmask=ip_netmask
-> set prendingipgateway=ip_gateway
-> set commitpending=true